## Slide 1: Silent Shredder: Zero-Cost Shredding For Secure Non-Volatile Main Memory Controllers
Amro Awad (NC State University)
Pratyusa Manadhata (Hewlett Packard Labs)
Yan Solihin (NC State University)
Stuart Haber (Hewlett Packard Labs)
William Horne (Hewlett Packard Labs)
ASPLOS 2016 2-6th April

## Slide 2: Outline
Background
Related Work
Goal
Design
Evaluation
Summary
Notes: The talk will be organized as follows: First we will start with a quick background, then discussing the goal of work design. Later we discuss the related work, followed by our design and evaluation. Finally, I will present a brief summary.

## Slide 3: Outline
Background
Related Work
Goal
Design
Evaluation
Summary

## Slide 4: Emerging NVMs
Emerging NVMs are promising replacements for DRAM.
  Fast (comparable to DRAM).
  Dense.
  Non-Volatile: persistent memory, no refresh power.
Examples:
  Phase-Change Memory (PCM).
  Memristor.
Source: http://www.techweekeurope.co.uk/
Notes: Emerging NVMs are promising replacement for DRAM: They are fast ___ dense ___ and non-volatile, hence no refresh power. Examples of such promising technologies are: Phase-Change Memory (PCM) and Memristor.

## Slide 5: Emerging NVMs
NVMs have their drawbacks:
  Limited endurance (e.g., PCM has ~108 writes per cell).
  Slow writes (e.g., PCM has ~150ns write latency).
  Data Remanence attacks are easier!
Requirements for using NVMs:
  Encrypt Data.
  Reduce number of writes, e.g., DCW and Flip-N-Write.
Encryption reduces efficiency of DCW and Flip-N-Write
Notes: Unfortunately, NVMs have their drawbacks: they have limited endurance __, slow write __, Data Remanence attacks: since NVMs are non-volatile anyone can remove the DIMMs and scan their data. Accordingly, deploying NVMs requires: __ Encrypting data, __ Reducing number of writes. As example, DCW is the technique that compares previous cell values and disable programming unchanged bits.

## Slide 6: Data Shredding
Data Shredding: The operation of zeroing out memory to avoid data leak.
  It prevents data leak between processes or virtual machines.
  Expensive:
    Up to 40% of page fault time could be spent in zeroing pages.
    For tested graph analytics apps, about 41.9% of memory writes could result from shredding.
Notes: Now lets talk about data shredding: data shredding is the operation of zeroing out memory to avoid data leak. As example, assume you have a page process A no longer needs memory page X. Later, process B want to allocate a page, the kernel must shred that data by zeroing out the page to avoid data leak. As mentioned earlier, the problem is that NVM writes are slow and limited!

## Slide 7: Example of Data Shredding
VM
NVM
Hypervisor
1- Request allocation
2- Zero out
Process
Process
OS
3- Request allocation
4- Zero out
VM

## Slide 8: How to implement shredding?
Technique | No cache pollution | Low-processor time | No Bus Traffic | No Memory Writes | Persistent
Regular stores | ✗ | ✗ | ✗ (indirectly) | ✗ (indirectly) | ✗
Non-Temporal Stores | ✔ | ✗ | ✗ | ✗ | ✔
DMA-Support Non-Temporal Bulk Zeroing [Jiang, PACT09] | ✔ | ✔ | ✗ | ✗ | ✔
RowClone (DRAM specific) [Shehadri, MICRO 2013] | ✔ | ✔ | ✔ | ✗ | ✔
Can we shred without writing?

## Slide 9: Threat Model
Physical access to the memory.
Snoop memory bus.
Notes: So first, lets discuss the threat model we assume. We assume a trusted processor, however, an attacker can have physical access to the memory devices, add memory snoopers on the memory bus. This assumption is similar to recent research papers on encrypted memory.

## Slide 10: Encryption/Decryption Process
Encryption/Decryption: CTR-mode.
The IV must change every time you encrypt new data.
Key insight: IV used for encryption = IV used for decryption.
Initialization Vector (IV)
Last-level Cache (LLC)
Encryption
Key
XOR
1- Cache line miss
2- Retrieve unique IV
3- Generate One-Time Pad (OTP)
NVM
Secure Area
3- Submit read request
4- Receive from NVM
5- Return decrypted
Notes: To do encryption and decryption, similar to recent proposals we use counter mode encryption. It works as following: assume you have a cache line miss, you need to retrieve a unique IV for that cache line.

## Slide 11: Initialization Vectors
We use Split-Counter Scheme [C. Yan, ISCA 2006] :
Cache line 0
512-bits
4KB Page (64 Cache lines)
Cache line 1
512-bits
Cache line 63
512-bits
…
Major (per page)
…
64-bit
7-bit
7-bit
…
7-bit
Major
Minor
Cache line address
IV
Padding
Notes: To be able to decrypt the data, we need to keep track of the IVs used to encrypt the cache lines. To do so, we use split-counter scheme proposed in ISCA 2006. Every page, lets say 4KB page will have 64-bit major counter shared across all cache lines. Every cache line will have 7 bit minor counter. The counters of the page are organized as 64B cache block.

## Slide 12: Typical Shredding
Counter Cache
Write encrypted
Zero Page X
NVM
Encryption/
Decryption
Read & update counters
Non-temporal Bulk Shredding
Page X
0000000000
Notes: So back to data shredding, data shredding will simply write encrypted zero page to the shredded page. In contrast, Silent Shredder, cleverly updates the IV value to make the previous page value unintelligible. if the IV value is changed, then it is cryptographically impossible to decrypt the data

## Slide 13: Our Proposal: Silent Shredder
Key idea: instead of zeroing shredded page, make it unintelligible
  By changing the key or IV prior to decryption
Design options:
  Have a key for every process
    Impractical: the memory controller needs to know process ID.
    Shared data requires same key.
  Increment all minor counters of a page
    Increases re-encryption frequency: minor counters will overflow faster.
  Increment the major counter

## Slide 14: Software Compatibility
To achieve software compatibility, would like to have zero cache lines for new/shredded pages.
Shredding: Increment major counter and zero all minor counters.
Zero-filled cache lines are returned for zeroed minor counters.
When minor counter overflows, it starts from 1.

## Slide 15: Design
Proc
Memory
Controller
+1
P
Cache and Coherence Controller
Counter
Cache
Tag
Major Ctr
Minor counters
0
0
0
0
0
0
1. Shred p
3. Increment M reset m1 … m64
5. Done
2. Invalidate p
4. Acknowledge

## Slide 16: Design
Counter
Cache
Tag
Major Ctr
Minor counters
=0?
NVMM
MC
Dk
MUX
LLC
00..0
2. Read the minor counter of the block x
3b. Yes
3a. No: fetch x
4. Return the fetched block
Or a zero-filled block
1. Miss x

## Slide 17: Evaluation Methodology
To evaluate our design, we use Gem5 to run a modified kernel.
  Added shred command to execute inside kernel’s clear_page function.
Baseline uses non-temporal stores bulk zeroing.
We use multi-programmed workloads from SPEC 2006 and PowerGraph suites.
Warm up 1B then run 500M instructions on each core (~4B overall) from initialization and graph construction phases.
We assume battery-backed Counter Cache.
Notes: - To evaluate our design, we use Gem5 to run a modified kernel.
- We use a baseline of non-temporal stores bulk zeroing shredding.
We use workloads from SPEC2006 and Powergraph suites.
For applications, data shredding mostly occur at initialization and graph construction phases. Accordingly, we run 500M instructions on each core (~4B overall) from initialization and graph construction phases.

## Slide 18: Configurations
Processor | CPU | 8-Cores, X86-64, 2GHz clock
 | L1 Cache | 2 cycles, 64KB size, 8-way, LRU, 64B block size
 | L2 Cache | 8 cycles, 512KB size, 8-way, LRU, 64B block size
 | L3 Cache | Shared, 25 cycles, 8MB size, 8-way, LRU, 64B block size
 | L4 Cache | Shared 35 cycles, 64MB size, 8-way, LRU, 64B block size
Main Memory (NVM) | Capacity | 16GB
 | # Channels | 2 channels
 | Channel bandwidth | 12.8 GB/s
 | Read/Write latency | 75ns/150ns
 | IV Cache | 10 cycles, 4MB capacity, 8-way associativity, 64B blocks
Operating System | OS | Gentoo
 | Kernel | 3.4.91

## Slide 19: Characterization

## Slide 20: Results
50.3% read traffic reduction
46.5% (Very high shredding)
48.6% write reduction
44.6% (very high shredding)

## Slide 21: Results
6.4% IPC Improvement
19.3% (very high shredding)
3.3x reads speed up
2.8x (very high shredding)
Notes: As we can see, some benchmarks got good performance improvement, but others didn’t. On average 6.4% IPC improvement was observed.

## Slide 22: Other Use Cases
  Bulk zeroing: Silent Shredder can be used for initializing large areas.
  Large-Scale Data Isolation: Fast data shredding for isolation across VMs or isolated nodes.
  Fast and efficient virtual disk provisioning when using byte-addressable NVM devices.
  Garbage collectors in managed programming languages.

## Slide 23: Summary
We eliminate writes due to data shredding.
Our scheme is based on manipulating IV values.
Silent Shredder leads to write reduction and performance improvement.
Applicable to other cases.

## Slide 24
            Thanks!
            Questions

## Slide 25: Encryption Assumption
Encryption: CTR-mode.
Same IV should never be reused for encryption.
OTP generation doesn’t need the data.
Initialization Vector (IV)
Encryption
Global Key
XOR
Ciphertext
Plaintext
One Time Pad (OTP)

## Slide 26: Security Concerns
Any IV-based encryption scheme needs to guarantee the following:
  Counter Cache Persistency
    Counters must be kept persistent either by battery-backed, using write-through cache or using NVM-based counter cache.
  IVs’ and Data Integrity
    IVs and Data must be protected from tampering/replaying.
    Authenticated encryption, e.g., Bonsai Merkle Tree, can be used.

## Slide 27: Backup slides

## Slide 28: Costs of Data Shredding
Increasing overall number of main memory writes.
  Our experiments showed that up to 42% of main memory writes can result from shredding.